|  |  | Legislation/Codes of Practice |
| --- | --- | --- |
| SWMS 13 |  | OH&S Act 2000, OH&S Regulation 2001, Excavation Work (WorkCover Code of Practice), Moving Plant on Construction Sites (WorkCover Safety Guide). |
| BULK EXCAVATION/ EARTHWORKS |  | Training required to complete work |
|  |  | All persons are to be inducted into this SWMS, with any special training requirements identified prior to this induction. |
|  |  | Personnel & Qualifications |
|  |  | All operators of machinery are to have WorkCover accredited tickets. |
|  |  | Inspection/ Maintenance on Plant/Equipment before use |
| PERSON RESPONSIBLE FOR SWMS IMPLEMENTATION |  | All plant is to be inspected by the operator on a daily basis using Robson’s Daily Plant Inspection Checklist. |
|  |  | Risk Rating Matrix Table |
| Name | Position |  | Critical – C 1 - 3 High – H 4 - 10 Moderate – M 11 - 15 Low – L 16 -25 |
|  | Project Manager |  |  |
|  | Site Manager |  | Severity of Consequences |
|  |  | Could kill, permanently disable or cause very serious damage. Could cause serious injury (major LTI) or major damage. Could cause typical LTI / MTC or moderate damage. Could cause 1st Aid injury or minor damage Couldn’t cause injury or damage |
| Issue No | Issue Date | Amendments/Remarks |  |  |
|  |  |  |  | Probability of Happening |
|  |  |  |  | A – ALMOST CERTAIN to happen B – LIKELY to happen at some point C – MODERATE – possible, it might happen D – UNLIKELY, not likely to happen E – RARE, practically impossible |

Approved:														Date:

| Induction Record. This Safe Work Method Statement has been shown and explained to me. I understand these procedures and I agree to abide by them. |
| --- |
| Inductors Initials: | Name: | Signature: | Date: | Inductors Initials: | Name: | Signature: | Date: |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Locate Services | Hit live above and under ground services (power, water, gas). | C | 1 | 4 | REFER SWMS PL-01 – “WORKING UNDER POWER LINES” | D | 1 | 7 | Site Manager |
| 2 | Stripping topsoil & bulk earthworks including stockpiling | Mechanical failure. | B | 3 | 9 | Plant & Truck inspections are to be current, with any problems reported to the workshop. Unsafe plant/truck is NOT to be operated. | D | 3 | 17 | Site Manager, All Workers |
|  |  | Moving plant/ trucks striking a worker or member of public. | C | 2 | 8 | Keep personnel & public clear of plant/truck. Reversing beepers & flashing lights are to be operating. Workers to wear highly visible clothing & keep 10m clear of moving plant or tipping truck. Signal to operator/driver before moving into the operating/tipping area. Don’t push over stockpiles. | D | 2 | 12 | Site Manager, All Workers |
|  |  | Moving plant colliding. | C | 2 | 8 | When operating machinery be aware of operation at hand, and plant movements. | D | 2 | 12 | Site Manager, All Workers |
|  |  | Excessive noise from operating plant. | C | 4 | 18 | Plan exhausts are to be properly maintained. Hearing protection for operators & spotters. | D | 4 | 21 | Site Manager |
|  |  | Excavation collapse. | C | 2 | 8 | Batter excavations. | D | 2 | 12 | Site Manager |
|  |  | Fuel spillage. | C | 4 | 18 | Provide bunded area for refuelling. | D | 4 | 21 | Site Manager |
| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| 3 | Load trucks using loaders & excavators. | Falling debris hits worker or cab. | C | 2 | 8 | Stand 5m clear of swinging radius of plant, and load over rear of truck. | D | 2 | 12 | Site Manager, All Workers |
|  |  | Plant overturning causing injury to operator, and damage to plant. | C | 2 | 8 | Ensure that the ground from which loading is stable or alter SWMS if unstable conditions encountered. Ensure all plant has ROPS fitted. | D | 2 | 12 | Site Manager |
| 4 | Haul to stockpile area & tip. | Dust. | C | 4 | 18 | Provide water cart, and sediment control. | D | 4 | 21 | Site Manager |
|  |  | Tipping truck overturning. | C | 2 | 8 | Tip on level compacted ground. Keep personnel & public clear of truck. Workers to wear highly visible clothing and keep 10m clear of tipping truck. | D | 2 | 12 | Site Manager |
| 5 | Hauling off site or importing fill | Truck colliding with local traffic. | C | 2 | 8 | Traffic signage & control to be in accordance with RTA guidelines (ticketed traffic controller and traffic control plan refer to TC-01) | D | 2 | 12 | Site Manager |
|  |  | Sediment escaping into stormwater system. | C | 3 | 13 | Install environmental controls as necessary. Install a suitable truck wash facility prior to hauling from site | D | 3 | 17 | Site Manager |
| 6 | Hydraulic Hammering of batters or excavations | Dust | C | 4 | 18 | Utilise water carts Wear dust mask | D | 4 | 21 | Site Manager |
|  |  | Noise | C | 4 | 18 | Ensure equipment is maintained and inspected Wear earplugs or muffs for P.P.E | D | 4 | 21 | Site Manager, All Workers |
|  |  | Flyrock | C | 4 | 18 | Ensure work area is clearly partitioned off | D | 4 | 21 | Site Manager |
| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| 7 | Communication on site | Collision with machines or vehicles on site | C | 2 | 8 | All personnel must call on Channel 16 before passing any machine When crossing RDS, check with Traffic Controllers to make sure it is safe to pass | D | 2 | 12 | Site Manager, All Workers |
| 8 | Working at Night | Workers on ground | B | 2 | 5 | Ground workers to wear reflective safety vests or overalls with reflective tape Ensure operators are fully aware of presence before ground workers move into operating radius of plant equipment Site Managers to impress upon all workers the need to take additional precautions due to visibility limitations | D | 2 | 12 | Site Manager, All Workers |
|  |  | Vision | B | 3 | 9 | Additional precautions with reflective safety vests/uniforms/overalls to be worn Erect additional artificial lighting at work areas | D | 3 | 17 | Site Manager |
|  |  | Fatigue | C | 2 | 8 | All workers to have had prescribed rest period before commencing night works Workers to be given adequate warning of change from day shift to night shift to allow and compensate for sleep pattern adjustments | D | 2 | 12 | Site Manager, All Workers |
| 9 | Operating plant equipment fitted with seat belts | Plant overturns | C | 1 | 4 | Provide training & supervision to ensure seat belts are worn at all times | D | 1 | 7 | Site Manager |

| No. | Activity | Potential Hazards | P | C | Risk | Control Measures | P | C | Risk | Person Responsable |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |